## Slide 1: Representation of signed numbers

## Slide 2: 3 WAYS
sign magnitude representation
2. 1’s complement form
3. 2’s complement form

## Slide 3
Computers must represent everything with binary digits.
It is customary to represent the sign with a bit placed in the leftmost position of the number.
The convention is to make the sign bit 0 for positive and 1 for negative.

## Slide 4: 1. Sign Magnitude representation
To represent a positive binary number (+n) and a negative (-n) binary number, we can use them with the addition of a sign.
For signed binary numbers the most significant bit (MSB) is used as the sign bit.

## Slide 5
Positive Signed Binary Numbers
Negative Signed Binary Numbers

## Slide 6: Disadvantage of Sign Magnitude Representation
The disadvantage here is that whereas before we had a full range n-bit unsigned binary number, we now have an n-1 bit signed binary number giving a reduced range of digits from:
-2(n-1) to +2(n-1)
So for example: if we have 4 bits to represent a signed binary number, (1-bit for the Sign bit and 3-bits for the Magnitude bits), then the actual range of numbers we can represent in sign-magnitude notation would be:
-2(4-1) – 1 to +2(4-1) – 1
-2(3) – 1 to +2(3) – 1
-7 to +7
Whereas before, the range of an unsigned 4-bit binary number would have been from 0 to 15,ie -2(n) to +2(n) to , we now have a reduced range of -7 to +7 ie -2(n-1) to +2(n-1)

## Slide 7: 2. 1’s Complement of a Signed Binary Number
1’s Complement as it is also termed, is another method which we can use to represent negative binary numbers in a signed binary number system.
In 1’s complement, positive numbers (also known as non-complements) remain unchanged as before with the sign-magnitude numbers.
The 1’s complement of a negative binary number is the complement of its positive counterpart.
To take the 1’s complement of a binary number, all we need to do is change each bit in turn. Thus the 1’s complement of “1” is “0” and vice versa,
e.g 1’s complement of 100101002 is 011010112

## Slide 8: 1’s Complement Using Inverters

## Slide 9
one’s complement can also have n-bit notation to represent numbers in the range from: -2(n-1) and +2(n-1) – 1.
For example, a 4-bit representation in the one’s complement format can be used to represent decimal numbers in the range from -7 to +7 with two representations of zero: 0000 (+0) and 1111 (-0) the same as before.

## Slide 10: 3. 2’s Complement of a Signed Binary Number
2’s Complement is another method to represent negative binary numbers in a signed binary number system.
In 2’s complement form, a negative number is the 2’s complement of its positive number with the subtraction of two numbers being A – B = A + ( 2’s complement of B ) ,
2’s complement is 1’s complement + 1.

## Slide 11
consider the number 9, represented in binary with eight bits.
+9 is represented 00001001.
Although there is only one way to represent +9, there are three different ways to represent -9 with eight bits:
signed‐magnitude representation: 10001001
signed‐1’s‐complement representation: 11110110
signed‐2’s‐complement representation: 11110111

## Slide 12: 4-bit Signed Binary Number Comparison
Decimal | Signed Magnitude | Signed One’s Complement | Signed Two’s Complement
+7 | 0111 | 0111 | 0111
+6 | 0110 | 0110 | 0110
+5 | 0101 | 0101 | 0101
+4 | 0100 | 0100 | 0100
+3 | 0011 | 0011 | 0011
+2 | 0010 | 0010 | 0010
+1 | 0001 | 0001 | 0001
+0 | 0000 | 0000 | 0000
-0 | 1000 | 1111 | –
-1 | 1001 | 1110 | 1111
-2 | 1010 | 1101 | 1110
-3 | 1011 | 1100 | 1101
-4 | 1100 | 1011 | 1100
-5 | 1101 | 1010 | 1011
-6 | 1110 | 1001 | 1010
-7 | 1111 | 1000 | 1001
Referred by www.electronics-tutorials.ws