## Slide 1: CODE CONVERTERS

## Slide 2
Code converter – takes an input code, translates to its equivalent output code.
Code
converter
Input
code
Output
code
Example: Binary to Gray code converter
  Input: Binary
  Output: Gray
Gray to Binary
  Input: Gray
  Output: Binary
BCD to Excess-3 code converter.
  Input: BCD code
  Output: Excess-3 code

## Slide 3: BINARY TO GRAY & GRAY TO BINARY
Binary to Gray
  Record the most significant bit as it is.
  EX-OR this bit to the next position bit, record the resultant bit.
  Record successive EX-ORed bits until completed.
  Convert 0011 binary to Gray.
g3 = b3
g2 = b3 xor b2
g1 = b2 xor b1
g0 = b1 xor b0

## Slide 4: BINARY TO GRAY & GRAY TO BINARY
Gray to Binary
The Gray code can be converted to binary by a reverse process.
Record the most significant bit as it is.
EX-OR binary MSB to the next bit of Gray code and record the resultant bit.
Continue the process until the LSB is recorded.
Convert 1011 Gray to Binary code.
Equations Are:
b3 = g3
b2 = g3 xor g2 or b3 xor g2
b1 = g3 xor g2 xor g1 or b2 xor g1
b0 = g3 xor g2 xor g1 xor g0 or b1 xor g0

## Slide 5: BCD-TO-EXCESS-3 CONVERTER
Truth table:
 | BCD |  |  |  | Excess-3 |  |  | 
 | A | B | C | D | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
2 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
5 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
6 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
8 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
9 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
10 | 1 | 0 | 1 | 0 | X | X | X | X
11 | 1 | 0 | 1 | 1 | X | X | X | X
12 | 1 | 1 | 0 | 0 | X | X | X | X
13 | 1 | 1 | 0 | 1 | X | X | X | X
14 | 1 | 1 | 1 | 0 | X | X | X | X
15 | 1 | 1 | 1 | 1 | X | X | X | X
K-maps:
1
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
W
1
1
1
1
1
1
1
1
1
1
1
1
1
1
X
Y
Z

## Slide 6: BCD-TO-EXCESS-3 CONVERTER
W = ?
X = ?
Y = ?
Z = ?
1
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
Z
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
W
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
X
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
Y
