## Slide 1: Combinational Logic Circuit Comparator

## Slide 2: Contents
Introduction of Comparator
Types
Comparator IC
Cascading Comparator
Applications

## Slide 3: Introduction
Comparator
  Compare two input signal or values and produce output depends on conditions on inputs.
  Compare 2 binary numbers to find out which one is greater than or smaller than or equal to other number.
  A A>B
  A = B
  B A<B

## Slide 4: Comparator
Types
  Identity Comparator
  Magnitude Comparator
    1-bit
    2-bit
    4-bit

## Slide 5: Comparator
Identity Comparator
  A digital comparator that has only one output terminal for when A = B either ―HIGH (A = B = 1) or LOW (A = B = 0).
Magnitude Comparator
  A digital comparator which has three output terminals, one each for equality, A = B greater than, A > B and less than A < B.

## Slide 6: Magnitude Comparator
1-bit Magnitude Comparator
  Two single bit numbers compared and 3 outputs to generate less than, greater than or equal to between two numbers.
Inputs |  | Outputs |  | 
A | B | A > B | A = B | A < B
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0

## Slide 7: Magnitude Comparator
2-bit Magnitude Comparator
  Compare 2 bit binary numbers and 3 outputs to generate less than, greater than or equal to between two numbers.
Inputs |  |  |  |  | Outputs |  |  | 
A1 | A0 | B1 |  | B0 | A > B |  | A = B | A < B
0 | 0 | 0 | 0 |  |  | 0 | 1 | 0
0 | 0 | 0 | 1 |  |  | 0 | 0 | 1
0 | 0 | 1 | 0 |  |  | 0 | 0 | 1
0 | 0 | 1 | 1 |  |  | 0 | 0 | 1
0 | 1 | 0 | 0 |  |  | 1 | 0 | 0
0 | 1 | 0 | 1 |  |  | 0 | 1 | 0
0 | 1 | 1 | 0 |  |  | 0 | 0 | 1
0 | 1 | 1 | 1 |  |  | 0 | 0 | 1
1 | 0 | 0 | 0 |  |  | 1 | 0 | 0
1 | 0 | 0 | 1 |  |  | 1 | 0 | 0
1 | 0 | 1 | 0 |  |  | 0 | 1 | 0
1 | 0 | 1 | 1 |  |  | 0 | 0 | 1
1 | 1 | 0 | 0 |  |  | 1 | 0 | 0
1 | 1 | 0 | 1 |  |  | 1 | 0 | 0
1 | 1 | 1 | 0 |  |  | 1 | 0 | 0
1 | 1 | 1 | 1 |  |  | 0 | 1 | 0

## Slide 8: K map for A< B

## Slide 9: Comparator IC
Comparator IC used to compare 1-bit, 2-bit or 4-bit binary numbers.
If numbers are more than 4-bit, we require 2 or more 7485 IC’s.

## Slide 10: Cascading Comparator
When we want to compare more than 4-bit number by cascading 2 or more 4-bit comparators is called as Cascading comparator.
Lower comparator outputs are used as cascading inputs for upper comparator.

## Slide 11: Application of Comparator
Process controller
Null detector
Password verification
Used in CPUs